## Slide 1: Minimal Instruction Set Processor for Basic Arithmetic and Logic Operations
Team Name: CompArch Kids
Team Members:
Sameeth (23114017)
Sonika (23114019)
Raviteja (23114040)
Koushik (23114063)
Aasish Varma (23114069)

## Slide 2: Project Overview
Goal: Design a 32-bit processor capable of basic arithmetic, logic operations.
Key Features:
  Compact and flexible Instruction Set Architecture (ISA).
  Arithmetic and Logical Operations.
  Modular Design for Future Expandability.

## Slide 3: Instruction Set Architecture (ISA)
Definition: Describes semantics of all processor instructions.
General Instruction Format:
3-bit opcode.
1-bit immediate flag.
5-bit register addressing.
Up to 18-bit immediate/offset.
Supported Formats:
3-address, 2-address, 1-address.

## Slide 4: ALU Operations
Supported Operations:
  ADD OR
  SUB MUL
  AND MOV
Immediate and Register-Based Instructions:
  ADD R1, R2, #7 vs ADD R1, R2, R3.

## Slide 5: Design Components
Instruction Fetch Unit:
Fetches instructions from memory.
Memory Unit:
Stores instructions and data.
Register File:
32 registers with read/write functionality.
Arithmetic Logic Unit (ALU):
Performs arithmetic and logic operations.

## Slide 6: Hardware Implementation
Simulation Tools:
EDA Playground: Verified logic functionality.
Quartus Prime Lite: Visualized hardware components.
Hardware Components Visualized:
Data Path.
ALU and Registers.

## Slide 7: Key Modules Explained
Ripple Carry Adder:
Handles addition/subtraction.
Booth’s Multiplier:
Performs signed multiplication.
ALU:
Modular operations based on control signals.
Register File:
Read and write operations.

## Slide 8: Results and Insights
Simulation Results:
Functional verification of ALU operations.
Hardware Synthesis:
Detailed understanding of data flow and processor architecture.

## Slide 9: Challenges and Learnings
Challenges:
Synchronizing components for accuracy.
Ensuring efficient data flow.
Learnings:
Comprehensive understanding of processor design.
Importance of modularity in hardware systems.

## Slide 10: Future Enhancements
Add more complex instructions (e.g., division, floating-point operations).
Introduce branching, conditional branching and techniques to make it hazard free.
Optimize for power and performance.

## Slide 11: Conclusion
Summary:
Designed a minimal, efficient processor architecture.
Successfully implemented and tested core functionalities.
Acknowledgment: Team contributions and tools used.

## Slide 12: References and Links
Include links to:
  EDA Playground simulations.
  Quartus Prime hardware visualizations.
  Relevant project files on Google Drive.